## Slide 1: Simultaneous Information Flow Security and Circuit Redundancy in Boolean Gates
Ryan Kastner (kastner@ucsd.edu)
Department of Computer Science & Engineering
University of California San Diego

## Slide 2: Embedded Everywhere
Critical infrastructure increasingly connected to the web
Increasing integration and “software” everywhere
Notes: Kevin Fu Umass Amherst
Yoshi Kohno (UW), Stefan Savage (UCSD)

## Slide 3: Security is Important
Boeing 787 has shared ARINC 629 bus
Flight Control Network
Passenger Network
“The proposed architecture of the 787 […] allows new kinds of passenger connectivity to previously isolated data networks connected to systems that perform functions required for the safe operation of the airplane. Because of this new passenger connectivity, the proposed data network design and integration may result in security vulnerabilities from intentional or unintentional corruption of data and systems critical to the safety and maintenance of the airplane.” FAA, 14 CFR Part 25 [Docket No. NM364]
High-assurance systems must be verifiably:
Secure, Reliable, and Predictable
Notes: …like Banks. In banks, machines often execute programs that compute on highly sensitive secret data
And they want an assurance that these programs do not leak any secrets to the open nclassified network.
Similarly, aircrafts have the converse problem. As part of the Integrated Modular Avionics, more and more
Programs of mixed criticality are sharing the same computing infrastructure, and it is imperative that the critical
Programs be completely isolated from the useful, but not critical ones. The problem in the first case is termed
Confidentiality, while the second one is its dual, and termed Integrity. ‘
Both these problems generalize to the notion of information flow tracking, and require that information be
Marked as either confidential vs unclassified, or trusted vs untrusted, and then its flow should be tracked through the program to ensure that the two are either kept separate, or only the desired flows are happening.
However, as opposed to a general purpose context, high assurance systems introduce a completely new
Set of challenges.
High assurance systems have very strict policies on information flow.
Eventually personal system (corporate wiki, antivirus, powerpoint?) 
Real World Systems Examples just before glift intro.
Confidentiality, Integrity, and policies. Both have been shown in red.
Several high assurance sstems place a very high demand on security.
Military aircraft: Versatile Integrated Avionics
This work is motivated by the demands of high assurance systems. Boeing 777, the aircraft, has a common network for all data. This includes
Avionics data and network data for the users.
VIA hosts some 1.75 million lines of applications source code. This includes partitions written by Honeywell, Lockheed Aeronautics and Lockheed Systems Integration-Owego, but executed under Honeywell's operating system.
Information flow tracking is a technique developed to provide this security. (other way around)
This technique involves associating some security tags with each piece of data in the program, and then
tracking this information as the program executes. IFT is an integral component of these systems.
Transition: For such high assurance systems, we want three features from an information flow tracking system.
Ideal: Use Information Flow
20 years in development
Transition on Denning and Denning on lattices and IFT

## Slide 4: Security is Expensive
RedHat Linux: Best Effort Safety (EAL 4+)
  $30-$40 per LOC
Integrity RTOS: Design for Formal Evaluation (EAL 6+)
  $10,000 per LOC
  More evaluation of process, not end artifact
How did we end up this mess?
Notes: Green Hills Integrity RTOS

## Slide 5: Security is Hard (and getting worse)
The Good: Processing Capabilities are Scaling
  More cores / chip
  Faster performance through speculation, prediction, caching, parallelism
  Deeper system integration, custom functionality, and more feature rich software to run everywhere
The Bad: Increasingly Coupled Subsystems
  Predictors, caches, buffers, parallelism lead to complex timing variations and complicated “definitions of correctness”
  Systems are increasingly coupled
The Ugly: System Complexity Growing
  Execution increasingly non-deterministic
  Evaluation complexity growing dramatically
Core
Core
Predictors and Hidden State
Special Purpose Logic / Interconnect

## Slide 6: Previous Approaches to Secure Systems
Prog. Language
Logic Gates
Functional Units
Microarchitecture
Instruction Set
Compiler/OS
Applications
Volpano96, Jif99, Slam98, FlowCaml03
HiStar 06, Flume 07, Laminar 09
Taintcheck 04, LIFT 06, Dytan 07
DIFT 04, Minos 04, LBA 06, Raksha 07
Cache-flush: Osvik et. al. 2006...
BP Scrub: Aciicmez et al. 2007...
Exe Normalize: Kocher 1996…
Cache Rand: Lee et al. 2005...
Notes: Not attacks, but preventions
Integrity doesn’t guarantee. (instead of vulnerable).
$10K/LOC: doesn’t account for above attacks
Security is traditionally a top down affair
Is the application a good idea, does it in the best case conform to accepted policy and common sense
Is the implementation secure, including the interaction with the OS. Can we avoid buffer overflows, do we scrub SQL requests, etc.
But as we care more and more about secrecy and integrity, more and more questions come up about the trustworthiness of the underlying implementation. What is an “implementation” and “refinement”

## Slide 7: Properties Cross Abstractions
Security, Realtime, and Safety properties are a function of interactions across levels of abstraction which makes evaluation, debugging, optimization, and analysis very difficult
Applications
Language
Logic Gates
Microarchitecture
Instruction Set
Compiler/OS
Security Properties

## Slide 8: Our Approach to Secure Systems
Prog. Language
Logic Gates
Functional Units
Microarchitecture
Instruction Set
Compiler/OS
Applications
GLIFT: Providing a Secure Foundation
Bit-Tight Building Blocks (Control, Logic, Memory)
Execution Lease Architecture
Secure I/O and
Micro-Kernel
Design
Methodologies
Provably Secure
Application Properties
Notes: Not attacks, but preventions
Integrity doesn’t guarantee. (instead of vulnerable).
$10K/LOC: doesn’t account for above attacks
Security is traditionally a top down affair
Is the application a good idea, does it in the best case conform to accepted policy and common sense
Is the implementation secure, including the interaction with the OS. Can we avoid buffer overflows, do we scrub SQL requests, etc.
But as we care more and more about secrecy and integrity, more and more questions come up about the trustworthiness of the underlying implementation. What is an “implementation” and “refinement”

## Slide 9: Formalizing Information Flow
Trusted vs. Untrusted Tasks
  Trusted: processes which are critical to the correct functionality of the systems
  Untrusted: anything whose malfunction will not cause a problem
Enforce the property of non-interference:
  Verify information never flows from high to low.
  Untrusted information is never used to make critical (trusted) decisions nor to determine the schedule (real-time)
Technique for general lattice policies
  e.g., Secret = High, Unclassified = Low
System
Which Affects?
User Data
OUT
(Flight Control)
Trusted
OUT
(Trusted or Untrusted?)
Flight Data
Untrusted
Unclassified
Secret

## Slide 10: Information Flow: Inverter
a | o
0/T
1/T
1/U
0/U
0
0
0
0
1
1
1
0
Notes: There is a change in the output whenever there is a change in the input.

## Slide 11: Gate Level Information Flow Tracking
AND
What Affects?
b
o
at
ot
a
bt
(Trusted or
Untrusted?)
Trusted
Untrusted
u | v | w
0T | 0U | 0T
0U | 1U | 0U
0T | 0T | 0T
0U | 1T | 0U
Partial Truth Table
0U/T: Untrusted/Trusted ‘0’
1U/T: Untrusted/Trusted ‘1’
0T
0U
0T
0U
1T
0U
The output will be marked as untrusted when at least one untrusted input can influence the output
0T | 0U | 0T
0U | 1T | 0U
u =(a, at)
v =(b, bt)
AND
GLIFT
AND
w=(o, ot)
Notes: To understand how information flows are tracked at the gate level, consider the complex system in the previous example to be a simple AND gate. Inputs a and b are assigned bit-level labels a_t and b_t indicating their trust-level. The output will take the most restrictive label whose associated data affects the output o. For a better understanding, consider the first row of partial truth table, where a is trusted 0 and b is untrusted 0. Both inputs have an influence on the output. However, trusted is a more restrictive label. Thus, the output should be marked as trusted. Then consider the fourth row, where a is untrusted 0 and b is trusted 1. Input a determines the value of the output. Thus, the output should be marked as untrusted. We can see that the output will be marked as untrusted when at least one untrusted input has an influence on the output. For an n-input logic function, its GLIFT logic has 2n inputs. Thus, the synthesis of GLIFT circuits is far more complex.

## Slide 12: Gate Level Information Flow Tracking
a
b
o
b
a
o
b
u
u
a
u
(a)
(c)
# | a | b | au | bu | o | ou
1: | 0 | 0 | 0 | 1 | 0 | 0
2: | 0 | 1 | 0 | 1 | 0 | 0
3: | 1 | 0 | 0 | 1 | 0 | 1
4: | 1 | 1 | 0 | 1 | 1 | 1
(b)
Partial Truth Table
GLIFT Logic
  Wei Hu, Jason Oberg, Ali Irturk, Mohit Tiwari, Timothy Sherwood, Dejun Mu and Ryan Kastner, "On the Complexity of Generating Gate Level Information Flow Tracking Logic", IEEE Transactions on Information Forensics and Security, vol. 7, no. 3, June 2012
Notes: U = untrusted. Which is the same as tainted. Doing this to try to avoid confusion.

## Slide 13: Does this low level tracking help?
CLK
RESET
D
Q
010101…
Simple assumption that “bad inputs” always leads to “bad outputs” is overly conservative
1-bit Counter
Notes: What does it mean to track?
Reset tag is not hardcoded. Comes from some logic

## Slide 14: Safely Resetting the Counter
CLK
RESET
D
Q
010101…
1-bit Counter
Simple assumption that “bad inputs” always leads to “bad outputs” is overly conservative
Notes: What does it mean to track?
Reset tag is not hardcoded. Comes from some logic

## Slide 15: GLIFT Composition
b
a
o
s
t
o
a
s
a
t
t
s
b
s
b
t
t
s
a
b
s
o

## Slide 16: Execution Lease Architecture
Instr Mem
+4
jump target
R1
R2
through decode
PC
Predicates
Register File
old value
Data Memory
high low
Lease
Unit
Timer PC Memory
0
1
0
1
timer expired?
Restore PC
Information contained in space-time sandbox
  Mohit Tiwari, Xun Li, Hassan M G Wassel, Frederic T Chong, and Timothy Sherwood. “Execution Leases: A Hardware-Supported Mechanism for Enforcing Strong Non-Interference”, Proceedings of the International Symposium on Microarchitecture (Micro), December 2009
Notes: Make the data-path blue.
Untrusted can set bounds, but not overwrite.
Mem block prevents red from overwriting blue.
Show nesting of stack somehow.

## Slide 17: Secure I/O (I2C)
Restrict bus access
  Prevents explicit flows
Reset Master
  Prevents implicit timing flows
Master
Slave 1
(U)
Slave 2
(T)
Slave N
(T)
SDA
SCL
. . . .
ST
AD
AK
Adapter
Adapter
Adapter
Mutually Exclusive
Execution Lease
Adapter Clock
Reset
. . . .
  Jason Oberg, Wei Hu, Ali Irturk, Mohit Tiwari, Timothy Sherwood, and Ryan Kastner, "Information Flow Isolation in I2C and USB", Design Automation Conference (DAC), June 2011

## Slide 18: Full System
Untrusted
Device
VDD
SDA
SCL
I/O Bus
I/O Adapter
I/O Adapter
Trusted
Device
Context Switch
Scheduling
IPC
I/O
Separation Kernel
Trusted
Untrusted
Unclassified
Secret
runtime
runtime
Software
set PC timer
set mem bounds
set partitionID
in/out
ISA
lastPC
PC Lease Stack
Mem Lease Stack
$ Partition Logic
Kernel Mode
I/O Master Controller
Pipe Flush
Fetch
Decode
Execute
Commit
Instr Cache
Data Cache
Other u-arch
structures
CPU
On Chip
Memory
  Mohit Tiwari, Jason Oberg, Xun Li, Jonathan K Valamehr, Timothy Levin, Ben Hardekopf, Ryan Kastner, Frederic T. Chong, and Timothy Sherwood, "Crafting a Usable Microkernel, Processor, and I/O System with Strict and Provable Information Flow Security", International Symposium of Computer Architecture (ISCA), June 2011

## Slide 19: Generating GLIFT Logic
A constructive method
  Constructing a library containing GLIFT logic for gates.
  Synthesizing logic circuits to gate level netlist.
  Generating GLIFT logic constructively by mapping the netlist to the library.
Boolean gates
GLIFT library
GLIFT circuit
Gate level netlist
Logic function
Notes: GLIFT logic for digital circuits can be generated in three steps.

## Slide 20: GLIFT Logic Composition
b
a
o
s
t
o
a
s
a
t
t
s
b
s
b
t
t
s
a
b
s
o

## Slide 21: “Naïve” GLIFT Encoding
A data bit and its label are encoded separately.
  Variables: V = (a, at)
  Alphabet: α = {0T, 0U, 1T, 1U}, | α | = 4
  Encoding: E = {00, 01, 10, 11}
Drawbacks
  Redundant symbols in the alphabet: the value of an untrusted variable can be ignored in label propagation[Oberg DAC′10].
  Area, delay and simulation time overheads: complex GLIFT logic for primitive gates.
  High design complexity: the GLIFT logic and original circuit are nested.
Notes: Now let’s take a look at the existing encoding technique for GLIFT. In the existing encoding, a data bit and its label are encoded as separately as a pair (a, a_t). The alphabet contains 4 symbols, i.e., trusted 0, untrusted 0, trusted 1 and untrusted 1. The binary codes assigned to these symbols are 00, 01, 10, 11 respectively. We have observed that there are some drawbacks with the existing encoding. Firstly, the alphabet contains redundant symbols because the value of an untrusted variable can be ignored in label propagation. Secondly, the existing encoding introduces large area, delay and simulation time overheads resulting from complex GLIFT logic for primitive gates who are basic building blocks of large GLIFT circuits. Finally, high design complexity. Under the existing encoding technique, the GLIFT logic and the original circuit are nested because the GLIFT circuit requires intermediate wires from the original design. Now that the existing encoding technique has some drawbacks, we propose an improved encoding scheme for GLIFT logic representation.

## Slide 22: Improved GLIFT Encoding
Combine 0U and 1U to XU (untrusted don’t-care).
  Variables: V′ = (A1, A0)
  Alphabet: α′ = {0T, 1T, XU} , |α′| = 3
  Encoding: E′ = {00, 11, 01}
  Reasons for choosing E′
  Best among 24 possible schemes for primitive gates
  Separation of the GLIFT logic and original circuit
  Enabling circuit redundancy
Notes: The new encoding technique combines the untrusted 0 and untrusted 1 symbols in the old alphabet to untrusted don’t-care, i.e. X_U. Now that these two symbols are combined to a single one, the number of symbols in the new alphabet has been reduced to 3. It is quite necessary to point out that this reduction is based on the inherent property of GLIFT and thus cannot be found by a logic synthesizer. Further, this reduction is more important than assigning binary codes to the symbols in the new alphabet itself. We encode the symbols in the new alphabet as 00, 11 and 01 respectively. There are several reasons for choosing the encoding E prime. First of all, it is the best among all 24 possible encoding schemes for the primitive gates. Secondly, the GLIFT logic and the original circuit are separated rather than nested. Finally, this encoding enables circuit redundancy when there is no untrusted input. We will go in more detail on these.

## Slide 23: Naïve vs Improved GLIFT Encoding
Old encoding[Oberg DAC′10]
  AND/NAND-N:
  OR/NOR-N:
New encoding
  AND-N
  OR-N
  2-input gates
Notes: Under the old encoding technique, the GLIFT logic for n-input AND, NAND, OR and NOR gates are show by the two logic equations, where product is defined as logic AND operation and the minus sign means removing the last term from the equation. We can see that the number of product terms is exponential to the number of inputs, to be specific 2^n. Using the new encoding, the GLIFT logic for n-input AND and OR gates are simply two n-input AND and OR gates respectively. For a better understanding, let’s consider the GLIFT logic for some 2-input gates… The new GLIFT logic would be worse if a design contains a high percentage of invertors. Since the new GLIFT logic for the invertor are two invertors, the new GLIFT logic for n-input NAND and NOR gates are simply two n-input NAND and NOR gates. Further, we can consider more complex components such 2-input multiplexer. We need to use the GLIFT for AND, OR and NOT to construct tracking logic for a MUX-2. Since the GLIFT logic for primitive gates are simpler under the new encoding scheme. The tracking logic for MUX-2 will be more efficiently represented using the new encoding technique.

## Slide 24: Separation of GLIFT Logic
  The old GLIFT logic requires intermediate results from the original circuit, e.g., wire d.
  The new GLIFT logic is complete independent of the original design.
Notes: The old GLIFT logic requires intermediate wires from the original design. Thus, the GLIFT circuit and the original circuit are nested. Under the new encoding, the GLIFT logic contains all the information for taint propagation and is completely independent from the original design. This is very useful for static verification scenarios, where the GLIFT will be removed after the verification completes. It is also useful for 3-D integration of the GLIFT logic as a security layer since communication between the stacked security layer and the original circuit is significantly reduced.

## Slide 25: And Circuit Redundancy…
  The GLIFT logic is exactly twice the original circuit when there is no untrusted input, which implements triple modular redundancy (TMR) for fault tolerance.
Notes: Another highlight of the new encoding is that it enables circuit redundancy where there is no untrusted input. In this case, the GLIFT logic will be exactly twice the original design, which implements TMR for fault tolerance. As we known, fault tolerance is another important property that usually needs to be enforced in high assurance systems.

## Slide 26: Area Results
Chart: 
| ttt2 | alu2 | alu4 | vda | x1 | t481 | too_large
Original | 1 | 1 | 1 | 1 | 1 | 1 | 1
Old Encoding | 7.7813 | 4.9039 | 5.7095 | 4.9586 | 7.5895 | 8.752 | 10.849
New Encoding | 3.4479 | 2.8929 | 2.9999 | 3.041 | 3.6478 | 3.874 | 2.8676
On average 25.7% reductions in area on the 30 largest benchmarks tested
44.3%
59.0%
52.5%
61.3%
48.0%
45.3%
26.4%
Wei Hu, Jason Oberg, Dejun Mu, and Ryan Kastner, "Simultaneous Information Flow Security and Circuit Redundancy in Boolean Gates", International Conference on Computer-Aided Design (ICCAD), November 2012
Notes: We used some IWLS benchmarks for area, delay and simulation time analysis. The area results are normalized respect to the original benchmark. For example, the old GLIFT logic for ttt2 is about 7 and a half times of the original benchmark while its new GLIFT logic is about 3 and a half times. Percentage data in the graph show reductions in area achieved by the new encoding technique. On average 25.7% reductions in area is reported on the 30 largest circuits in the benchmark set.

## Slide 27: Delay Results
Chart: 
| ttt2 | alu2 | alu4 | vda | x1 | t481 | too_large
Original | 1 | 1 | 1 | 1 | 1 | 1 | 1
Old Encoding | 3.3385 | 2.9818 | 3.2917 | 3.2925 | 3.5577 | 3.15 | 3.3925
New Encoding | 1.4154 | 1.2636 | 1.1806 | 1.2358 | 1.25 | 1.2714 | 1.1505
On average 31.4% reductions in delay and 53.5% in area-delay product
42.4%
42.4%
35.9%
37.5%
35.1%
40.4%
33.9%
Wei Hu, Jason Oberg, Dejun Mu, and Ryan Kastner, "Simultaneous Information Flow Security and Circuit Redundancy in Boolean Gates", International Conference on Computer-Aided Design (ICCAD), November 2012
Notes: The new encoding also achieves significant improvements in delay. It has reported on average 31.4% reductions in delay and 53.5% in area-delay product on the 30 largest benchmarks tested.

## Slide 28: Simulation Time Results
Chart: 
| ttt2 | alu2 | alu4 | vda | x1 | t481 | too_large
Old Encoding | 5.1 | 5.33 | 9.87 | 13.93 | 15.35 | 45.1 | 88.9
New Encoding | 2.68 | 2.66 | 4.68 | 4.2 | 8.73 | 30.1 | 49.8
52.6%
49.9%
47.4%
30.2%
56.9%
66.7%
56.0%
Simulation time (min)
222 random vectors tested
Over 95% toggle coverage
On average 51.4% reduction in simulation time
Wei Hu, Jason Oberg, Dejun Mu, and Ryan Kastner, "Simultaneous Information Flow Security and Circuit Redundancy in Boolean Gates", International Conference on Computer-Aided Design (ICCAD), November 2012
Notes: GLIFT logic circuits in different encodings are simulated under the same number of random test vectors to get simulation time. In the test LFSR is used as random test vector generator. 2^22 benchmarks are tested for each benchmark and an over 95% percent toggle coverage is guaranteed. Experimental results show that GLIFT logic represented using the new encoding reports on average only half simulation time.

## Slide 29: Conclusion
GLIFT: A new technique for building systems with provable security properties
A set towards building security assertions into hardware
Untrusted
Device
VDD
SDA
SCL
I/O Bus
I/O Adapter
I/O Adapter
Trusted
Device
Context Switch
Scheduling
IPC
I/O
Separation Kernel
Trusted
Untrusted
Unclassified
Secret
runtime
runtime
Software
set PC timer
set mem bounds
set partitionID
in/out
ISA
lastPC
PC Lease Stack
Mem Lease Stack
$ Partition Logic
Kernel Mode
I/O Master Controller
Pipe Flush
Fetch
Decode
Execute
Commit
Instr Cache
Data Cache
Other u-arch
structures
CPU
On Chip
Memory